OpenLCB/NMRAnet
Developer and Early Adopter Kit
UNDERSTANDING DevKit Ios

The Ios in the DevKit have firmware loaded into them that does specific things. It makes use only of the Ios Input and Output connectors.

DevKit Ios are Special
In order to make the Ios in the DevKit immediately demonstrable, the Ios in the DevKit are programmed such that their inputs and outputs share the same event-numbers. This means that changes to inputs will be followed by the outputs of all boards. This is not typical Io behaviour, but we will show you how to revert the Ios to 'normal' behaviour.

Inputs
In response to a change in the voltage on an Input from 0V to 5V or 5V to 0V, the Io will send the event-number associated with state-change. For example, if you ground an input 0, then the Io will send a specific event-number, and will send a different one when you release the Input.

Outputs
Similarly, each Output is associated with two event-numbers. When the first of these is received from the network, the LED associated with that output will turn on, and the output go to ground. When the other event-number is received, the LED turns off and the output goes to +5V.

How DevKit Ios are Special
Normally, in an OpenLCB node, each input state and output state has its own unique event-numbers associated with it. In order to make the DevKit Ios immediately usable in a demo mode, every Io has the same event-number assigned to similarly numbered Inputs and Outputs, thus:
Default	On	Off
Input 0 and Output 0	05.02.01.02.02.00.00.00	05.02.01.02.02.00.00.01
Input 1 and Output 1	05.02.01.02.02.00.00.02	05.02.01.02.02.00.00.03
Input 2 and Output 2	05.02.01.02.02.00.00.04	05.02.01.02.02.00.00.05
Input 3 and Output 3	05.02.01.02.02.00.00.06	05.02.01.02.02.00.00.07
Input 4 and Output 4	05.02.01.02.02.00.00.08	05.02.01.02.02.00.00.09
Input 5 and Output 5	05.02.01.02.02.00.00.0A	05.02.01.02.02.00.00.0B
Input 6 and Output 6	05.02.01.02.02.00.00.0C	05.02.01.02.02.00.00.0D
Input 7 and Output 7	05.02.01.02.02.00.00.0E	05.02.01.02.02.00.00.0F

The consequences of this are that the Output LEDs of all Ios will follow the Input states of all Ios. This allows you to set up an interaction between Ios by simply plugging them together.
Restoring your Ios to Normal Behaviour.

Normally Ios have a set of event-numbers that are unique to each node and to each input and output state. They can be reset to this behaviour by holding down both the blue and gold buttons for 8 seconds. At about 3 seconds the blue and gold LEDs will start flashing rapidly – this is to warn you that a reload is taking place. Each time you do this a new set of unique event numbers will be loaded into the node.

Doing this the first time you perform this reload, it will result in the following event-numbers, where xx will be the last two digits of your Io node ID.

Default	On	Off
Input 0	05.02.01.02.02.xx.00.00	05.02.01.02.02.xx.00.01
Input 1	05.02.01.02.02.xx.00.02	05.02.01.02.02.xx.00.03
Input 2	05.02.01.02.02.xx.00.04	05.02.01.02.02.xx.00.05
Input 3	05.02.01.02.02.xx.00.06	05.02.01.02.02.xx.00.07
Input 4	05.02.01.02.02.xx.00.08	05.02.01.02.02.xx.00.09
Input 5	05.02.01.02.02.xx.00.0A	05.02.01.02.02.xx.00.0B
Input 6	05.02.01.02.02.xx.00.0C	05.02.01.02.02.xx.00.0D
Input 7	05.02.01.02.02.xx.00.0E	05.02.01.02.02.xx.00.0F
Output 0	05.02.01.02.02.xx.00.10	05.02.01.02.02.xx.00.11
Output 1	05.02.01.02.02.xx.00.12	05.02.01.02.02.xx.00.13
Output 2	05.02.01.02.02.xx.00.14	05.02.01.02.02.xx.00.15
Output 3	05.02.01.02.02.xx.00.16	05.02.01.02.02.xx.00.17
Output 4	05.02.01.02.02.xx.00.18	05.02.01.02.02.xx.00.19
Output 5	05.02.01.02.02.xx.00.1A	05.02.01.02.02.xx.00.1B
Output 6	05.02.01.02.02.xx.00.1C	05.02.01.02.02.xx.00.1D
Output 7	05.02.01.02.02.xx.00.1E	05.02.01.02.02.xx.00.1F

The next reload will produce:

Default	On	Off
Input 0	05.02.01.02.02.xx.00.20	05.02.01.02.02.xx.00.21
Input 1	05.02.01.02.02.xx.00.22	05.02.01.02.02.xx.00.23
Input 2	05.02.01.02.02.xx.00.24	05.02.01.02.02.xx.00.25
Input 3	05.02.01.02.02.xx.00.26	05.02.01.02.02.xx.00.27
Input 4	05.02.01.02.02.xx.00.28	05.02.01.02.02.xx.00.29
Input 5	05.02.01.02.02.xx.00.2A	05.02.01.02.02.xx.00.2B
Input 6	05.02.01.02.02.xx.00.2C	05.02.01.02.02.xx.00.2D
Input 7	05.02.01.02.02.xx.00.3E	05.02.01.02.02.xx.00.2F
Output 0	05.02.01.02.02.xx.00.30	05.02.01.02.02.xx.00.31
Output 1	05.02.01.02.02.xx.00.32	05.02.01.02.02.xx.00.33
Output 2	05.02.01.02.02.xx.00.34	05.02.01.02.02.xx.00.35
Output 3	05.02.01.02.02.xx.00.36	05.02.01.02.02.xx.00.37
Output 4	05.02.01.02.02.xx.00.38	05.02.01.02.02.xx.00.39
Output 5	05.02.01.02.02.xx.00.3A	05.02.01.02.02.xx.00.3B
Output 6	05.02.01.02.02.xx.00.3C	05.02.01.02.02.xx.00.3D
Output 7	05.02.01.02.02.xx.00.3E	05.02.01.02.02.xx.00.3F

And so on. You can do this 2000 times before you will run out of event-numbers.