Blue / Gold
Buttons and LEDs
Termination
Options
Optional I/O
Connectors
Reset Button
Output Connector
Position
Ouptut LEDs
Input Connector
Position
Power
Connector
Power
Options
LCB / CAN
Connectors
CAN Power
Options
Power
Indicator
Blue / Gold
Buttons and LEDs

DevKit
Manual
v0.1

<openlcb logo>
<railstars logo>
<nmranet logo>

Welcome to the OpenLCB / RailStars / NMRAnet DevKit. This kit is meant to allow you to quickly use it to solve a problem on your model railroad. This manual will help you with that task.

Contents:

1. Four Io version 1.0 nodes;
2. One USB-serial programming cable;
3. One manual (this);
4. A assortment of connectors:
5. Two 10-position screw-terminals;
6. Four shouded 2x5 headers;
7. Seven strips of pinheaders;
8. Four strips of 1x6 right-angle pinheader;

Please check to make sure you have these.

You will also need to supply a power-supply from 8-15VDC with a centre-positive barrel connector.

The Node as it appears out of the box.
Power:

The nodes can be supplied from three sources:
1. Externally from the 2mm Barrel connector. This requires 7-15VDC positive to inside. The USB Power Selector link needs to be set to “EXT”.
2. Externally through the Serial Connector. The USB Power Selector link needs to set to “USB”.
3. From the CAN / LCB bus. This requires the CAN Power Selector to be set to “CAN IN”.

Illustration 2: The CAN Power Selector.
Illustration 1: USB Power Selector

In addition, if the nodes are externally powered then they can provide power to the LCB / CAN bus , and other nodes, by setting the CAN Power Option link to the “CAN OUT” position.

.....

Output Connectors

  As from the box.

  Pinheaders installed.

  Screw-terminals installed.

......