# Protocol
22 Dec 2009
Mostly the number are not fixed and may change as the protocol is revised. So in general the names should be used instead of the numbers.
This only uses the 29 bit CAN extended header with normal frames.

:XpfdddsssNxx.....;

:X	USB or serial prefix of hex digit string for extended header. (S = short type not used.)
p	1 bit (most significant bit) priority, currently always 1.
f	4 bits frame type
ddd	12 bits destination node alias or broadcast message type
sss	12 bits source node alias.
N	Normal frame type, (R = RTR type not used.)
xx..	Data in hex pairs
;	end of packet string marker

### Frame Type

0x0	FT_CIM0	Top 12 bits of node ID
0x1	FT_CIM1	2nd top 12 bits of node ID
0x2	FT_CIM2	3rd top 12 bits of node ID
0x3	FT_CIM3	lowest 12 bits of node ID
0x4
0x5
0x6
0x7	FT_RIM	0x7FFF Sent by any node objecting to the node alias sent in a CIMn
0x8	See below	Broadcast frame type
0x9
0xA
0xB
0xC
0xD
0xE	See below	Destination Alias Addressed
0xF	Stream

### 0x8ddd Broadcast Packets

0x8000	FT_RESET	System reset, not yet implemented.
0x8001	FT_VNSN	Verify Node Serial Number, sent by anything that needs to know how to translate an alias to a full node id. Reply is several DAA_NSN packets.
0x8002	FT_INIT	Normal Initialization Complete, no data. / Should it send the full nodeID ?
0x8003	FT_BOOT	Similar to FT_INIT but only Boot Loader Initialization Complete.

Accessory
0x8010	FT_EVENT	8 bytes event code in the data
0x8011	FT_RFID	5 bytes RFID tag in the data

Track commands, not implemented yet.
0x8020	FT_TOF	Track Off, broadcast from CS
0x8021	FT_TON	Track On or Normal operation, broadcast from CS
0x8022	FT_ESTOP	Track Stopped (em. stop)
0x8023	FT_CSRESET	Command station Reset
0x8024	FT_RTOF	Request Track Off, from CAB
0x8025	FT_RTON	Request Track On or Normal operation, from CAB
0x8026	FT_RESTP	Request Emergency Stop ALL

CAB commands, not implemented yet.
0x8030	FT_RLOC	Request loco info
0x8031	FT_STMOD	Request speed step change
0x8032	FT_DSPD	Set Engine Speed/Dir
0x8033	FT_DFUN	Set engine functions
0x8034	FT_PLOC	Engine report from CS
0x8035	FT_PLOCF	Engine function report from CS
0x8036	FT_KLOC	Release loco

Consist commands, not implemented yet.
0x8037	FT_PCON	Consist Engine
0x8038	FT_KCON	Remove engine from consist

DCC programming, not implemented yet.
0x8040	FT_RDCC3	Request 3 byte DCC packet
0x8041	FT_RDCC4	Request 4 byte DCC packet
0x8042	FT_RDCC5	Request 5 byte DCC packet
0x8043	FT_RDCC6	Request 6 byte DCC packet

### 0xEddd Destination Alias Addressed
1st byte of data has message type.

0x00-0xFF	DAA_DATA	Sequence number in low 4 bits of the first byte, 7 bytes of data
0x10	DAA_ACK	Acknowledge with status in 2nd data byte.

0	ACK_OK	OK
1	ACK_CRC	CRC error, no longer used
2	ACK_TIMEOUT	timeout on data transfer, 2 seconds
3	ACK_NODATA	The requested data does not exist
4	ACK_NOSPACE	No space to store this data
5	ACK_ALIASERROR	Wrong Source Alias, probably 2 writes at the same time.

Program Loader
0x20	DAA_UPGSTART	Enter loader
0x21	DAA_UPGRESET	Clear program not loaded and re-boot
0x22	DAA_UPGREAD	Read 64 bytes, reply is enough DAA_DATA packets. / 24 bit address in data bytes.
0x23	DAA_UPGADDR	Write 64 bytes, followed by enough DAA_DATA packets. / 24 bit address in data bytes.

Events
0x30	DAA_CEERASEH	Consumer erase events, High 7 bytes of event in data.
0x31	DAA_CEERASEL	Consumer erase events, Low byte of event. If the 8 bytes of the event are all zero then erase everything
0x32	DAA_CEREADH	Consumer read events, High 7 bytes.
0x33	DAA_CEREADL	Consumer read events, Low byte, index, data length byte.
0x34	DAA_CEWRITEH	Consumer write event, High 7 bytes
0x35	DAA_CEWRITE	Consumer write event, Low byte, data length, up to 5 data bytes
0x36	DAA_PEERASE	Producer erase event, index
0x37	DAA_PEREAD	Producer read event, index
0x38	DAA_PEWRITEH	Producer write event, High 7 bytes
0x39	DAA_PEWRITEL	Producer write event, Low byte, index

Node variables
0x40	DAA_NVREAD	Read, 1 byte index
0x41	DAA_NVWRITE	Set, 1 byte index + 1 byte data
0x42	DAA_NVREPLY	Reply to read

Misc
0x50	DAA_NSN	Node serial number
0x51	DAA_DEFAULT	Reset (almost) everything to default values
0x52	DAA_REBOOT	Re-boot the module, after node ID write

### Node ID
All node id's should be unique, so that any node can be connected to all the others without causing a problem. A 48 bit node id was chosen to make this easy to achieve. For a MERG Kit, the buyer should be a MERG member, and used a node id formed as follows. The 1st byte = 3, the 2nd byte = 2, the 3rd to 5th bytes are the membership number and the last byte can have a unique value chosen by the member.

When initially programmed the bootloader initializes the node ID. However CAN only works with 2 nodes or more connected. So a USB or RS232 interface has an initial node ID = 000000000001 and other nodes have an initial node ID = 000000000002. Thus a network of 2 nodes can be constructed and the node id's changed before adding any more nodes.

If a larger network is constructed before setting the node id's, then it may be necessary to manually reboot each node (by shorting the MCLR pin to ground) to get unique node aliases.

### Node Alias
To get an initial node alias from the 48 bit node ID the 4 x 12 bit parts are xored together.

The 4 parts are transmitted using the FT_CIMn packets together with the alias. A 1 second timeout allows any node with the same alias to send a FT_RIM to object and cause the node to generate another alias.

To get the next alias the node ID is used as the initial seed for a 48 bit random number generator, the 4 x 12 bit parts are then xored together as before.

If 2 or more nodes have the same alias after the initial setup, then all nodes that detects the error should try to obtain a new unique alias by the method above.

The proposed 48-bit PRNG is from “A 48-Bit Pseudo-Random Number Generator”, Heidi G. Kuehn, Communications of the ACM, Volume 4, Issue 8 (August 1961), pages 350-352.

xi+1 = (29+1) xi + c

where c = 29,741,096,258,473 or 0x1B0CA37A4BA9.The paper actually describes a PRNG that uses signed arithmetic, but for our purposes the 48th “sign” bit isn't important.
Note that, unlike some other PNRGs, this one can generate a zero result, and can accept a zero seed.