# CANACC

One codebase for all 8 bit accessories using coditional compilation.

### CANACC4

From the PC the event action byte only uses the bottom 3 bit to select 1 of 8 outputs.
The output is a 100 msec pulse, followed by 600 msec CDU recharge time.

0	1A
1	1B
2	2A
3	2B
4	3A
5	3B
6	4A
7	4B

Teaching by switches. Set the L switch on and send an event.

0=on, 1=on, P=on	1A
0=on, 1=on, P=off	1B
0=off, 1=on, P=on	2A
0=off, 1=on, P=off	2B
0=on, 1=off, P=on	3A
0=on, 1=off, P=off	3B
0=off, 1=off, P=on	4A
0=off, 1=off, P=off	4B

The U switch on with the L switch on will remove an event.

Power on with the U switch on will erase all events.

### CANACC8 or CANACC5
The switches don't work because I don't have them yet.

From the PC the event action byte uses the bottom 5 bits.

0x00 – 0x07	The bottom 3 bits selects the output.
0x08	0 = off, 1 = on.
0x10	Toggle next bit in the opposite direction. Used for CANACC5 and slow motion point motors.

### CANACE8C
Not debugged yet.