# CANLED
10 Dec 2009

This is a module which can drive up to 64 LEDs.

At power up the module puts all the LEDs on for about 1 second.

In learn mode the led corresponding to the LED select switch is on. This is useful for testing as well.

For teaching from the PC, LED numbers are 0 to 63, or 0x00 to 0x3F. Events are stored as 9 bytes, the 8 byte event number and 1 byte action data. The action data byte of the event is 6 bits led number, 2 bits mode.
Where mode bits are 00 for off, 01 or 10 for flash, and 11 for on.
So add 64, 0x40, or 128, 0x80 for flashing, and 196, 0xC0 for on to the LED number.

Currently 3200 bytes are used for the table, which is 50 buckets of 64 bytes. Each 64 byte bucket holds 7 x 9 byte events. So 7 x 50 = 350 is the maximum number of events that could be stored.
In practice the table search slows at over 80% full, so a good maximum would be 280 events.

### Initial Testing
After construction, check the current taken at power up. After the initial capacitor charge pulse the current with all the chips is about 100mA.

The CAN bus needs to be connected to another module otherwise it will hang up trying to get a valid node ID alias and the green LED (LD1) will not come on.

The green LED (LD1) should come on at power up.

An led with the +ve longer lead in 9 and -ve shorter lead in 10 will be number 7. It should come on at power-up and after about 1 second it should go off.

Link the learn pins, the yellow led (LD2) should come on.
Set the led select switches to the first 3 (0,1,2) up and the second 3
 (3,4,5) down. LED7 should come on.
Send an on or off event.
Un-link the learn pins, LED7 and the yellow led goes out.
Send the on event again, LED7 comes on.
Send the off event, LED7 goes off.

If both the green and yellow LEDs come on then the module is either in boot loader mode or teach mode.

### Led number by D type pin connection
Pins 13 to 1 on the top row
pins 25 to 14 on the shorter row

The top row and first column are the D-type pin numbers.
The +ve side (longer lead) of the led goes to pin 10 to 13, the top row of the table.
The -ve side (flat side on the led base) goes to the pin in the first column.
The current is controlled by the driver chip so no series resistors are needed, and its possible to have 2 LED's in series in any/all position/s.

	Pin 10	Pin 11	Pin 12	Pin 13
Pin 2	0, 0x00	16, 0x10	32, 0x20	48, 0x30
Pin 3	1, 0x01	17, 0x11	33, 0x21	49, 0x31
Pin 4	2, 0x02	18, 0x12	34, 0x22	50, 0x32
Pin 5	3, 0x03	19, 0x13	35, 0x23	51, 0x33
Pin 6	4, 0x04	20, 0x14	36, 0x24	52, 0x34
Pin 7	5, 0x05	21, 0x15	37, 0x25	53, 0x35
Pin 8	6, 0x06	22, 0x16	38, 0x26	54, 0x36
Pin 9	7, 0x07	23, 0x17	39, 0x27	55, 0x37
Pin 21	8, 0x08	24, 0x18	40, 0x28	56, 0x38
Pin 20	9, 0x09	25, 0x19	41, 0x29	57, 0x39
Pin 19	10, 0x0A	26, 0x1A	42, 0x2A	58, 0x3A
Pin 18	11, 0x0B	27, 0x1B	43, 0x2B	59, 0x3B
Pin 17	12, 0x0C	28, 0x1C	44, 0x2C	60, 0x3C
Pin 16	13, 0x0D	29, 0x1D	45, 0x2D	61, 0x3D
Pin 15	14, 0x0E	30, 0x1E	46, 0x2E	62, 0x3E
Pin 14	15, 0x0F	31, 0x1F	47, 0x2F	63, 0x3F