# CANLCD
16 Jan 2010

Using a CANACC8 without the output driver chip to drive a 2 line LCD display.

The display I used had a Samsung S6A0069, but anything which is compatible with the Hitachi HD44780U should work.

The ULN2803 is replace by a 1k DIL resistor pack.

The 2 line LCD usually needs 5 volts power for the controller chip and back light.
Also a variable voltage is needed for the contrast control, this can be provided by a variable resistor connected across the 0v and 5v lines with the slider connected to the contrast input. The value is not very important, I used a spare 2k one that was also used for VR1 on the canacc8.

The display is used in 4 bit mode, so 4 data lines and 3 control lines need to be connected.

CANACC8 J3	LCD
pin1	5v
Pin2	D4
pin3	D5
pin4	D6
pin5	D7
pin6	RW
pin7	RS
pin8	E
pin9	not used
pin10	gnd

Make sure Pin1 has 5v, by adjusting the output of the LM317 or omit the LM317 and use the 5v supply instead.

The text message is displayed by sending a 64 byte data block to address 0x000000, which probably means a PC has to be used.

In C# the following will send a text message s to module with alias m. It also needs some code to determine the alias from the unique NodeID since the alias can change at any time.

static void sendblock(int m, string s)
{
    // address CAN packet
    can(":X1E" + hex(m, 3) + "001N" + hex((int)DAA.DAA_UPGADDR, 2) +"000000;");
    s = s.PadRight(65,'\0');
    for (int j = 0, a = 0; j < 10; j++, a+=7)
    { // send 9 data packets with 7 bytes and 1 with 1 byte.
        string canmsg = ":X1E" + hex(m, 3) + "001N";
        canmsg += hex((int)DAA.DAA_DATA | j, 2);
        canmsg += hex((byte)s[a], 2); // 7 bytes data
        if (j != 9)
        {
        canmsg += hex((byte)s[a + 1], 2);
        canmsg += hex((byte)s[a + 2], 2);
        canmsg += hex((byte)s[a + 3], 2);
        canmsg += hex((byte)s[a + 4], 2);
        canmsg += hex((byte)s[a + 5], 2);
        canmsg += hex((byte)s[a + 6], 2);
        }
        canmsg += ";";
        can(canmsg);
    }
}