# CANACE3
27 Nov 2009
This is a switch module for up to 128 switches or push buttons.
The hardware has a link J5 to select push button mode or switch mode. In switch mode up to 128 on/off type switches can be connected with diodes. In push button mode up to 128 push buttons or 64 center off non-latching switches can be used without diodes.
The address selection links and pushbutton S1 are not used.
After about 2 seconds in switch mode the module send the position of every switch at 1 every 20 msec, taking about 2.5 seconds. Since there are normally no switches closed in button mode this does not happen in button mode.
### 25 Pin D connector
The event is 6 bytes of node ID followed by 1 byte zero and 1 byte given by the following tables.
In switch mode:
	Pin14	Pin2	Pin15	Pin3	Pin16	Pin4	Pin17	Pin5
Pin18	0x00	0x01	0x02	0x03	0x04	0x05	0x06	0x07
Pin6	0x08	0x09	0x0A	0x0B	0x0C	0x0D	0x0E	0x0F
Pin19	0x10	0x11	0x12	0x13	0x14	0x15	0x16	0x17
Pin7	0x18	0x19	0x1A	0x1B	0x1C	0x1D	0x1E	0x1F
Pin20	0x20	0x21	0x22	0x23	0x24	0x25	0x26	0x27
Pin8	0x28	0x29	0x2A	0x2B	0x2C	0x2D	0x2E	0x2F
Pin21	0x30	0x31	0x32	0x33	0x34	0x35	0x36	0x37
Pin9	0x38	0x39	0x3A	0x3B	0x3C	0x3D	0x3E	0x3F
Pin22	0x40	0x41	0x42	0x43	0x44	0x45	0x46	0x47
Pin10	0x48	0x49	0x4A	0x4B	0x4C	0x4D	0x4E	0x4F
Pin23	0x50	0x51	0x52	0x53	0x54	0x55	0x56	0x57
Pin11	0x58	0x59	0x5A	0x5B	0x5C	0x5D	0x5E	0x5F
Pin24	0x60	0x61	0x62	0x63	0x64	0x65	0x66	0x67
Pin12	0x68	0x69	0x6A	0x6B	0x6C	0x6D	0x6E	0x6F
Pin25	0x70	0x71	0x72	0x73	0x74	0x75	0x76	0x77
Pin13	0x78	0x79	0x7A	0x7B	0x7C	0x7D	0x7E	0x7F

In button mode:
	Pin14	Pin2	Pin15	Pin3	Pin16	Pin4	Pin17	Pin5
Pin18	On 0x00	On 0x01	On 0x02	On 0x03	On 0x04	On 0x05	On 0x06	On 0x07
Pin6	Off 0x00	Off 0x01	Off 0x02	Off 0x03	Off 0x04	Off 0x05	Off 0x06	Off 0x07
Pin19	On 0x08	On 0x09	On 0x0A	On 0x0B	On 0x0C	On 0x0D	On 0x0E	On 0x0F
Pin7	Off 0x08	Off 0x09	Off 0x0A	Off 0x0B	Off 0x0C	Off 0x0D	Off 0x0E	Off 0x0F
Pin20	On 0x10	On 0x11	On 0x12	On 0x13	On 0x14	On 0x15	On 0x16	On 0x17
Pin8	Off 0x10	Off 0x11	Off 0x12	Off 0x13	Off 0x14	Off 0x15	Off 0x16	Off 0x17
Pin21	On 0x18	On 0x19	On 0x1A	On 0x1B	On 0x1C	On 0x1D	On 0x1E	On 0x1F
Pin9	Off 0x18	Off 0x19	Off 0x1A	Off 0x1B	Off 0x1C	Off 0x1D	Off 0x1E	Off 0x1F
Pin22	On 0x20	On 0x21	On 0x22	On 0x23	On 0x24	On 0x25	On 0x26	On 0x27
Pin10	Off 0x20	Off 0x21	Off 0x22	Off 0x23	Off 0x24	Off 0x25	Off 0x26	Off 0x27
Pin23	On 0x28	On 0x29	On 0x2A	On 0x2B	On 0x2C	On 0x2D	On 0x2E	On 0x2F
Pin11	Off 0x28	Off 0x29	Off 0x2A	Off 0x2B	Off 0x2C	Off 0x2D	Off 0x2E	Off 0x2F
Pin24	On 0x30	On 0x31	On 0x32	On 0x33	On 0x34	On 0x35	On 0x36	On 0x37
Pin12	Off 0x30	Off 0x31	Off 0x32	Off 0x33	Off 0x34	Off 0x35	Off 0x36	Off 0x37
Pin25	On 0x38	On 0x39	On 0x3A	On 0x3B	On 0x3C	On 0x3D	On 0x3E	On 0x3F
Pin13	Off 0x38	Off 0x39	Off 0x3A	Off 0x3B	Off 0x3C	Off 0x3D	Off 0x3E	Off 0x3F