# CANLED
26 Nov 2009

This is a module which can drive up to 64 LEDs.

At power up the module puts all the LEDs on for about 1 second.

In learn mode the led corresponding to the led select switch is on. This is useful for testing as well.

For teaching from the PC, LED numbers are 0 to 63. Events are stored as 10 bytes, the 8 byte event number and 2 byte action data. The event is taught using a 2 byte command, currently the second byte is ignored. The first byte of the event is 6 bits led number, 1 bit polarity, and 1 bit toggle.
So add 64 for Invert Polarity, and add 128 for Toggle mode to the led number.

### Initial Testing
After construction, check the current taken at power up. After the initial capacitor charge pulse the current with all the chips is about 100mA.

The CAN bus needs to be connected to another module otherwise it will hang up trying to get a valid node ID alias and the green LED (LD1) will not come on.

The green LED (LD1) should come on at power up.

An led with the +ve longer lead in 9 and -ve shorter lead in 10 will be number 7. It should come on at power-up and after about 1 second it should go off.

Link the learn pins, the yellow led (LD2) should come on.
Set the led select switches to the first 3 (0,1,2) up and the second 3
 (3,4,5) down. LED7 should come on.
Send an on or off event.
Un-link the learn pins, LED7 and the yellow led goes out.
Send the on event again, LED7 comes on.
Send the off event, LED7 goes off.

If both the green and yellow LEDs come on then the module is either in boot loader mode or teach mode.

### Led number by D type pin connection
Pins 13 to 1 on the top row
pins 25 to 14 on the shorter row

The top row and first column are the D-type pin numbers.
The +ve side (longer lead) of the led goes to pin 10 to 13, the top row of the table.
The -ve side (flat side on the led base) goes to the pin in the first column.
The current is controlled by the driver chip so no series resistors are needed, and its possible to have 2 LED's in series in any/all position/s.

	Pin 10	Pin 11	Pin 12	Pin 13
Pin 2	0	16	32	48
Pin 3	1	17	33	49
Pin 4	2	18	34	50
Pin 5	3	19	35	51
Pin 6	4	20	36	52
Pin 7	5	21	37	53
Pin 8	6	22	38	54
Pin 9	7	23	39	55
Pin 21	8	24	40	56
Pin 20	9	25	41	57
Pin 19	10	26	42	58
Pin 18	11	27	43	59
Pin 17	12	28	44	60
Pin 16	13	29	45	61
Pin 15	14	30	46	62
Pin 14	15	31	47	63