# RS232 or USB interface

This code is for the CANRS and CANUSB modules and uses the Grid Connect format for extended normal data CAN packets.

Before compiling the symbol USB or RS232 must be defined, this is done in the makefile.

For CANRS pins 1, 4, and 6 on the back of the 9 pin D type should be linked.

For CANRS this version has 256 byte serial buffers, enough for 12 CAN packets. It also uses ECAN in mode 2, so there are 8 hardware receive buffers and 3 transmit buffers. However, the RS232 serial connection is running at less than half the speed of the CAN bus, so with high traffic messages will be dropped.

Windows HyperTerminal can be used to view or send packets.

There are some extra text messages.

Start
At reset. Shows the CANRS/USB is talking to the PC.

-ECAN Buffer overflow-
If the ECAN buffer overflow flag is set when reading a CAN packet.

-ECAN Invalid message-
If the ECAN Invalid message fag is set when reading a CAN packet.

-ECAN TXERRCNT xx-
if the TXERRCNT changes. xx is the value of the count.

-ECAN RXERRCNT xx-
if the RXERRCNT changes. xx is the value of the count.

OK
if the text string sent to the CANRS/USB is placed in a transmit buffer.

Error
if there is no empty transmit buffer available (should never happen).
or if the text string sent to the CANRS/USB is not correctly formatted.

Too long
if the text string sent to the CANRS/USB is too long for a valid packet.

### Grid Connect Format

:X<header>N<data>;
<header> is:
1	the priority bit
xxxx	4 hex digits for the frame type
xxx	3 hex digits for the source node alias.
<data> a sequence of hex digit pairs, one pair for each data byte.