# OpenLCB for MERG CANACE3
4 Dec 2009
This is a switch module for up to 128 switches or push buttons. Since each switch can be either on or off the module can send up to 256 different event codes
If on/off type switches are used then diodes have to be inserted in the matrix to stop false keys being detected. If non-latching centre off switches or push buttons are used the diodes are not necessary.
The address selection links, J5 link and push button S1 are not used.
About 2 seconds after power up, the module sends the position of every switch. It sends these at a rate of 1 every 20 msec, taking about 2.5 seconds for all 128.
All modules must be initialized with a new node ID after building, the default node ID will be either 000000000001 or 000000000002.
To change the node ID connect the PC, press the “Com Port” button and select the com port used for the connection. Then press the “Get NID's” button for get a list of node ID's and aliases. On the Node tab, in the “Node Alias” drop down list select the alias of the new module this will probably be 001 or 002 unless there are several modules with the same node ID. Change to the “Node ID” tab and enter the correct globally unique number. For MERG users this is 3, 2 in the first two decimal boxes, your membership number in the box below the next 3 decimal boxes, and a unique serial number for the module which you can choose in the last decimal box. The press the “Write NID” button, followed by the “Reboot” button.
The module will then reboot and start using the new node ID. So press the “Get NID's” button again to get a new list of node ID's and aliases. On the Node tab, in the “Node Alias” drop down list select the new alias of the new module again. To set up the default events go the the “Producer Events” tab and click “Set Defaults”. If you need to change any event codes for the switches this can also be done on this tab. If you have a saved configuration to restore this can be done on the “Node” tab.
The default event is the 6 bytes of the node ID, 1 byte of zero, the index number of the switch as given in the following table and the least significant bit is 0 for off and 1 for on.
To reduce the start of day traffic, unused events can be deleted by setting them to 0xFFFFFFFFFFFFFFFF by selecting the index of the event and using the “Erase” button on the “Producer Events” tab.

### Switch Event Index - 25 Pin D connector
The most significant 7 bits of the index for the switches or push buttons is given by the following table. The least significant bit of the index is 0 for off and 1 for on.

	Pin14	Pin2	Pin15	Pin3	Pin16	Pin4	Pin17	Pin5
Pin18	0x00	0x02	0x04	0x06	0x08	0x0A	0x0C	0x0E
Pin6	0x10	0x12	0x14	0x16	0x18	0x1A	0x1C	0x1E
Pin19	0x20	0x22	0x24	0x26	0x28	0x2A	0x2C	0x2E
Pin7	0x30	0x32	0x34	0x36	0x38	0x3A	0x3C	0x3E
Pin20	0x40	0x42	0x44	0x46	0x48	0x4A	0x4C	0x4E
Pin8	0x50	0x52	0x54	0x56	0x58	0x5A	0x5C	0x5E
Pin21	0x60	0x62	0x64	0x66	0x68	0x6A	0x6C	0x6E
Pin9	0x70	0x72	0x74	0x76	0x78	0x7A	0x7C	0x7E
Pin22	0x80	0x82	0x84	0x86	0x88	0x8A	0x8C	0x8E
Pin10	0x90	0x92	0x94	0x96	0x98	0x9A	0x9C	0x9E
Pin23	0xA0	0xA2	0xA4	0xA6	0xA8	0xAA	0xAC	0xAE
Pin11	0xB0	0xB2	0xB4	0xB6	0xB8	0xBA	0xBC	0xBE
Pin24	0xC0	0xC2	0xC4	0xC6	0xC8	0xCA	0xCC	0xCE
Pin12	0xD0	0xD2	0xD4	0xD6	0xD8	0xDA	0xDC	0xDE
Pin25	0xE0	0xE2	0xE4	0xE6	0xE8	0xEA	0xEC	0xEE
Pin13	0xF0	0xF2	0xF4	0xF6	0xF8	0xFA	0xFC	0xFE