# OpenLCB for MERG CBUS Modules
13 Jan 2010
The aim is to provide OpenLCB protocol for MERG CBUS modules.

All modules need a unique node ID which can be assigned by the user from their MERG membership number.

In general:
The green led comes on when the module has initialized.
The yellow led and green led are on when the bootloader is being executed.
The yellow led pulses on when an event packet or a DAA packet to this module is seen.

# Protocol
Mostly the number are not fixed and may change as the protocol is revised. So in general the names should be used instead of the numbers.
This only uses the 29 bit CAN extended header with normal frames.

The order of packets is not fixed and may need to be corrected by the receiver.

:XpfdddsssNxx.....;

:X	USB or serial prefix of hex digit string for extended header. (S = short type not used.)
p	1 bit (most significant bit) priority, currently always 1.
f	4 bits frame type
ddd	12 bits destination node alias or broadcast message type
sss	12 bits source node alias.
N	Normal frame type, (R = RTR type not used.)
xx..	Data in hex pairs
;	end of packet string marker

### Frame Type
0x0	FT_CIM0	Top 12 bits of node ID, sent to test a new alias.
0x1	FT_CIM1	2nd top 12 bits of node ID, sent to test a new alias.
0x2	FT_CIM2	3rd top 12 bits of node ID, sent to test a new alias.
0x3	FT_CIM3	lowest 12 bits of node ID, sent to test a new alias.
0x4
0x5
0x6
0x7	FT_RIM	0x7FFF, sent by any node objecting to the node alias sent in a CIMn
0x8	See below	Broadcast frame type
0x9
0xA
0xB
0xC
0xD
0xE	See below	Destination Alias Addressed
0xF	Stream

### 0x8ddd Broadcast Packets
0x8000	FT_RESET	System reset, not yet implemented.
0x8001	FT_VNSN	Verify Node Serial Number, sent by anything that needs to know how to translate an alias to a full node id. Reply is several DAA_NSN packets.
0x8002	FT_INIT	Normal Initialization Complete, no data. / Should it send the full nodeID ?
0x8003	FT_BOOT	Similar to FT_INIT but only Boot Loader Initialization Complete.

Accessory
0x8010	FT_EVENT	8 bytes event code in the data
0x8011	FT_RFID	5 bytes RFID tag in the data

Track commands, not implemented yet.
0x8020	FT_TOF	Track Off, broadcast from CS
0x8021	FT_TON	Track On or Normal operation, broadcast from CS
0x8022	FT_ESTOP	Track Stopped (em. stop)
0x8023	FT_CSRESET	Command station Reset
0x8024	FT_RTOF	Request Track Off, from CAB
0x8025	FT_RTON	Request Track On or Normal operation, from CAB
0x8026	FT_RESTP	Request Emergency Stop ALL

CAB commands, not implemented yet.
0x8030	FT_RLOC	Request loco info
0x8031	FT_STMOD	Request speed step change
0x8032	FT_DSPD	Set Engine Speed/Dir
0x8033	FT_DFUN	Set engine functions
0x8034	FT_PLOC	Engine report from CS
0x8035	FT_PLOCF	Engine function report from CS
0x8036	FT_KLOC	Release loco

Consist commands, not implemented yet.
0x8037	FT_PCON	Consist Engine
0x8038	FT_KCON	Remove engine from consist

DCC programming, not implemented yet.
0x8040	FT_RDCC3	Request 3 byte DCC packet
0x8041	FT_RDCC4	Request 4 byte DCC packet
0x8042	FT_RDCC5	Request 5 byte DCC packet
0x8043	FT_RDCC6	Request 6 byte DCC packet

### 0xEddd Destination Alias Addressed
1st byte of data has message type.

General
0x00-0xFF	DAA_DATA	Sequence number in low 4 bits of the first byte, 7 bytes of data
0x10	DAA_ACK	Acknowledge with status in 2nd data byte.

0	ACK_OK	OK
1	ACK_CRC	CRC error, no longer used
2	ACK_TIMEOUT	timeout on data transfer, 2 seconds
3	ACK_NODATA	The requested data does not exist
4	ACK_NOSPACE	No space to store this data
5	ACK_ALIASERROR	Wrong Source Alias, probably 2 writes at the same time.

Program Loader
0x20	DAA_UPGSTART	Enter loader
0x21	DAA_UPGRESET	Clear program not loaded and re-boot
0x22	DAA_UPGREAD	Read 64 bytes, reply is enough DAA_DATA packets. / 24 bit address in data bytes.
0x23	DAA_UPGADDR	Write 64 bytes, followed by enough DAA_DATA packets. / 24 bit address in data bytes.

Events
0x30	DAA_CEERASEH	Consumer erase events, High 7 bytes of event in data.
0x31	DAA_CEERASEL	Consumer erase events, Low byte of event. If the 8 bytes of the event are all zero then erase everything
0x32	DAA_CEREADH	Consumer read events, High 7 bytes.
0x33	DAA_CEREADL	Consumer read events, Low byte, index, data length byte.
0x34	DAA_CEWRITEH	Consumer write event, High 7 bytes
0x35	DAA_CEWRITE	Consumer write event, Low byte, data length, up to 5 data bytes
0x36	DAA_PEERASE	Producer erase event, index
0x37	DAA_PEREAD	Producer read event, index
0x38	DAA_PEWRITEH	Producer write event, High 7 bytes
0x39	DAA_PEWRITEL	Producer write event, Low byte, index

Node variables
0x40	DAA_NVREAD	Read, 1 byte index
0x41	DAA_NVWRITE	Set, 1 byte index + 1 byte data
0x42	DAA_NVREPLY	Reply to read

Misc
0x50	DAA_NSN	Node serial number
0x51	DAA_DEFAULT	Reset (almost) everything to default values
0x52	DAA_REBOOT	Re-boot the module, after node ID write

### Node ID
All node id's should be unique, so that any node can be connected to all the others without causing a problem. A 48 bit node id was chosen to make this easy to achieve. For a MERG Kit, the buyer should be a MERG member, and use a node id formed as follows. The 1st byte = 3, the 2nd byte = 2, the 3rd to 5th bytes are the membership number and the last byte can have a unique value chosen by the member.

When initially programmed the bootloader initializes the node ID. However CAN only works with 2 nodes or more connected. So a USB or RS232 interface has an initial node ID = 000000000001 and other nodes have an initial node ID = 000000000002. Thus a network of 2 nodes can be constructed and the node id's changed before adding any more nodes.

If a larger network is constructed before setting the node id's, then it may be necessary to manually reboot each node (by shorting the MCLR pin to ground) to get unique node aliases.
##### Node Alias
To get an initial node alias from the 48 bit node ID the 4 x 12 bit parts are xored together.

The 4 parts are transmitted using the FT_CIMn packets together with the alias. A 1 second time out allows any node with the same alias to send a FT_RIM to object and cause the node to generate another alias.

To get the next alias the node ID is used as the initial seed for a 48 bit random number generator, the 4 x 12 bit parts are then xored together as before.

If 2 or more nodes have the same alias after the initial setup, then all nodes that detects the error should try to obtain a new unique alias by the method above.

The proposed 48-bit PRNG is from “A 48-Bit Pseudo-Random Number Generator”, Heidi G. Kuehn, Communications of the ACM, Volume 4, Issue 8 (August 1961), pages 350-352.

xi+1 = (29+1) xi + c

where c = 29,741,096,258,473 or 0x1B0CA37A4BA9.The paper actually describes a PRNG that uses signed arithmetic, but for our purposes the 48th “sign” bit isn't important.

Note that, unlike some other PRNGs, this one can generate a zero result, and can accept a zero seed.

# Memory Layout
##### Boot memory layout
The boot loader uses the bottom 4k of program memory.
0x000000	Reset, test the program loaded flag and execute the program or the loader
0x000008	High priority interrupt, always redirected to the program.
0x000018	Low priority interrupt, always redirected to the program.
0x000020	7 byte version info for boot loader
0x000030	jump to loader, called from the program.
0x000040	6 byte Node ID (low first), 6 byte random seed, 2 bytes alias, 50 bytes empty
0x000080	64 byte block, boot loader text string
0x0000C0	64 byte block, user identification string

##### Program memory layout
Program start address = 0x1000.
0x001000	redirected reset
0x001008	redirected high priority interrupt
0x001018	redirected low priority interrupt
0x001020	7 byte version info for program
0x001027	valid program loaded flag, 0xFF=no program, 0x00=valid program
0x001028	4 bytes start address of XML data description file
0x00102C	2 bytes length of XML file.
0x00102E	18 spare bytes
0x001040	64 byte block with program identification string

Note. In C18, 16 and 32 bit (2 and 4 byte) data are stored low byte first. Addresses are 24 bits. OpenLCB data is store most significant byte first.
# Program loading
There are 3 versions of the loader, one for loading from CAN interface, one for USB interface and one for loading from RS232 interface. Most modules will use the CAN version.
The PC side will only send data above the 4k boot loader area. In order to change the boot loader a program has to be loaded which will check the new code is complete and then copies the new boot loader over the old one. Finally setting the program loaded flag so it does not get executed again after a reset.
A new program is sent 64 bytes at a time. The first write should be the first 64 bytes of the new program with the valid program loaded flag set to 0xFF.
To enter the boot loader a DAA_UPGSTART is sent, after the program halts interrupts and jumps to the loader a DAA_ACK with ACK_OK is sent back to the PC.
Each 64 byte block starts with DAA_UPGADDR and is followed by 10 DAA_DATA packets. After writing the block the loader will send DAA_ACK with ACK_OK to signal that the next block can be sent. The blocks can be received in any order so they should be stored on a buffer until all the packets are received.
After all the program blocks have been successfully sent, a DAA_UPGRESET is sent from the PC to clear the valid program loaded flag and restart the program.
# Event teaching from PC
All modules should respond to these packets even if they have no event data.

The packets for event teaching from the PC all use Destination Alias Addressed packets, with the first byte of the data containing a type code for the rest of the data bytes.

For general I/O modules there may be both producer and consumer events to handle, so two sets of commands are used.

Consumer events are looked up using the 8 byte event number, producer events are looked up by an index formed from the input.

Some limits for event data:
Always 8 bytes for the event number.
Up to 65000 events per module, but most modules use much less than this.
Up to 64 bytes for the event data so it can use the same buffer as the loader, most modules will only use 1 or 2 bytes.
##### Event Packet Types
DAA_CEERASEH	Erase consumer events, the high 7 bytes of the event code.
DAA_CEERASEL	Erase consumer events, the low byte of the event code.
DAA_CEREADH	Read consumer events, the high 7 bytes of the event code.
DAA_CEREADL	Read consumer events, the low byte, event index and data length.
DAA_CEWRITEH	Write consumer event, the high 7 bytes of the event code.
DAA_CEWRITEL	Write consumer event, Low byte and the index.

DAA_PEERASE	Erase producer event given by the index.
DAA_PEREAD	Read producer events, event index.
DAA_PEWRITEH	Write producer event, the high 7 bytes of the event code.
DAA_PEWRITEL	Write producer event, Low 1 bytes and the index.

DAA_DEFAULT	Initialize events and node variables to default values.
DAA_DATA	Up to 7 bytes of data per packet, block of up to 64 bytes. see boot loader document.
DAA_ACK	Ack with status, see boot loader document.
##### Set default
DAA_DEFAULT:	no data.
Re-initialize the producer events and node variables to the default values.
Default producer events are the node ID followed by the switch or input number and the on or off state.
The reply should be DAA_ACK = OK, even if there is nothing to do.
##### Consumer Erase Event data
DAA_CEERASEH:	7 high bytes of event
DAA_CEERASEL:	last byte of event

For a consumer, the node should erase all events that match the event number. If the event number is zero then it erases all events. The reply should be DAA_ACK = OK, even if there is nothing to do.
##### Producer Erase Event data
DAA_PEERASE:	2 byte index

For a producer, the event number is not used, the event at the index is erased. The reply is DAA_ACK = OK, or DAA_ACK = NOSPACE if the index is out of range.

##### Consumer Event read
DAA_CEREADH:	7 high bytes of event
DAA_CEREADL:	last byte of event, 2 byte index,

If the event number is zero then read all events. The first read should have index = 0. Each read should increase the index until the error return NODATA is received. This returns one event, in DAA_CEWRITEH, DAA_CEWRITEL and a number of DAA_DATA packets. The index is used to decide which event to read if there is more than one set of event data with a matching event number. The module should send an error reply DAA_ACK = NODATA if there is no data corresponding to this index or DAA_ACK = TIMEOUT if a packet gets lost .
##### Producer Event read
DAA_PEREAD:	2 byte index

A producer will ignore the event number and just use the index. This returns one event, in DAA_PEWRITEH, DAA_PEWRITEL. The module should send an error reply DAA_ACK = NODATA if there is no data corresponding to this index.
##### Consumer Event write
DAA_EVWRITEH:	7 high bytes of event
DAA_EVWRITEL:	last byte of event, 1 byte data length, 5 bytes data

The event number is never zero. If the number of bytes of data that will follow is 5 or less, then the data is in the packet. If the number of bytes is more than 5 then all the data is in data packets. The module should send DAA_ACK = OK after storing the data, or DAA_ACK = TIMEOUT if a packet gets lost, or DAA_ACK = NOSPACE if there is no space to store it.
##### Producer Event write
DAA_EVWRITEH:	7 high bytes of event
DAA_EVWRITEL:	last byte of event, 2 bytes index

The event number is never zero. The index is use to decide which event is replaced. The module should send DAA_ACK = OK after storing the data, or DAA_ACK = TIMEOUT if a packet gets lost, or DAA_ACK = NOSPACE if there is no space to store it.