# RFID
30 Jan 2010

This uses the MERG CBUS CANRS board with the MERG RFID reader board and Core ID series reader.
Serial BAUD is 9.6 kb/s
Reader format is <STX 02> <10 bytes of hex data> <2 byte xor of data> <cr> <lf> <ETX 03>

To use the CANRS hardware the RFID output needs to be connected to pin 3 instead of pin 2 on the CANRS and the gender of the D-type needs changing.

The OpenLCB output is packets with frame type FT_RFID, the node ID alias is in the 12 source ID bits, and 5 bytes RFID tag in the data. Anything which needs the location of the reader as well as the RFID tag needs to monitor changes in the alias for the node ID's. Either by following the CIM packets or by using the FT_VNSN and DAA_NSN packets.

A short program in C# to display information from known RFID tags or display the hex code for unknown ones. This works for a single reader, for more readers it would be neccesary to add code to handle the node ID alias to full node ID and location lookup. The current program output is:

Com port opened
03: 21ft SR 12t 8 Plank
08: 20ft BR 16t Mineral
Tag 0104A151CE
Tag 0104A17C55

using System;
using System.Collections.Generic;
using System.Text;
using System.IO.Ports;

namespace rfid
{
    class Program
    {
        // copy and paste in frametypes.c

        static Dictionary<string, string> rfids = new Dictionary<string, string>();
        static System.IO.Ports.SerialPort com;
        static string line = "";

        static void waitloop()
        {
        while (true)
        {
        // CAN input
        line += com.ReadExisting();
        // ignore anything before :
        int l = line.IndexOf(':');
        if (l == -1)
        continue;
        line = line.Substring(l);
        // find a complete CAN packet
        l = line.IndexOf(';');
        if (l == -1)
        continue;
        string packet = line.Substring(0, l + 1);
        line = line.Substring(l + 1);
        FT sw = (FT)Convert.ToInt32(packet.Substring(3, 4), 16);
        switch (sw)
        {
        case FT.FT_RFID:
        string tag = packet.Substring(11, 10);
        try
        {
        tag = rfids[tag];
        }
        catch (KeyNotFoundException)
        {
        tag = "Tag " + packet.Substring(11, 10);
        }
        Console.WriteLine(tag);
        break;
        }
        }
        }

        static void Main(string[] args)
        {
        com = new SerialPort("COM8", 11520);
        try
        {
        com.Open();
        Console.WriteLine("Com port opened");
        }
        catch
        {
        Console.WriteLine("Com port failed to opened");
        return;
        }
        rfids.Add("0104A1781E", "01: 21ft LNER 12t Van");
        rfids.Add("0104A13F0A", "02: 21ft LNER 12t 6 Plank");
        rfids.Add("0104A181F2", "03: 21ft SR 12t 8 Plank");
        rfids.Add("0104A17C34", "04: 21ft SR 12t Van");
        rfids.Add("0104A15AF2", "05: 21ft LMS Van D1832A");
        rfids.Add("0104A17BBD", "06: 21ft LMS Van D1832A");
        rfids.Add("0104A13725", "07: 21ft LMS 12t Open");
        rfids.Add("0104A18181", "08: 20ft BR 16t Mineral");
        rfids.Add("0104A15BBA", "09: 27ft SR 25t Brake");
        rfids.Add("0104A169B2", "10: 21ft GWR 12t 5 Plank");

        waitloop();

        }
    }
}